## Slide 1: Math Module 1
Rates of Change
& Mathematical Models

## Slide 2: STEM Technology
What is Technology?
  The collection of implements that are created using human ingenuity.
Examples:
  Spear
  Dish washer
  Computer
  Oven
  Bridge
  etc.

## Slide 3: STEM Engineering
What is engineering?
  The design of technological implements.
In order to efficiently design these implements it is very helpful to know how nature works and to be able to predict what will happen in a given situation.
Examples:
  Electricity
  Mechanics
  Biology
  Etc.

## Slide 4: STEM Science
What is science?
  The study of the laws of nature.
The understanding these laws (at least imperfectly) is the underpinning of engineering and ultimately technology.
In order to make predictions about what will happen in nature, it is necessary to do the following:
  Make observations.
  Create models that explain/predict the observed phenomena.
  Test these models by making predictions and testing them against new observations.

## Slide 5: STEM Mathematics
What is mathematics?
  A collection of logical tools that can be used in the study of patterns.
We see patterns and problems repeated in many different disciplines.
Mathematics gives us generalized tools to study similar problems without regard discipline.

## Slide 6: Mathematical Robot Models
With Legos it is easy to experiment by snapping together bricks, writing computer code and seeing what happens.
A Lego robot might be used as a model for a more sophisticated purpose built robot.
There are an extremely large number of possible combinations, however, so it is very helpful to have a model to give you a good place to start.
Designing non-Lego robots could be very expensive and a large number of experiments might be prohibitive.
Studying the properties of our robots and building mathematical models can make our designs much more efficient.

## Slide 7: Distance Time
Suppose we have a robot that is driving away from a wall.
The distance from the wall is measured by an Ultrasonic Sensor.
The distance is measured every 0.04 seconds over a period of 1 second.
The program to do this is wall1.py and is available on the workshop Wikispaces site. We will learn how to write code like this in the workshop.

## Slide 8: Distance Time
The following table contains the measured distances and times.
What is the velocity of the robot?
Time (sec) | Distance (cm) | Time (sec) | Distance (cm) | Time (sec) | Distance (cm)
0 | 3 | 0.36 | 13.7 | 0.72 | 28.8
0.04 | 3 | 0.4 | 14.9 | 0.76 | 30.8
0.08 | 3.2 | 0.44 | 17 | 0.8 | 32.6
0.12 | 4 | 0.48 | 18.5 | 0.84 | 32.8
0.16 | 5.8 | 0.52 | 19.8 | 0.88 | 33.6
0.2 | 6.7 | 0.56 | 21.2 | 0.92 | 35.5
0.24 | 9.3 | 0.6 | 23.5 | 0.96 | 36.5
0.28 | 10.3 | 0.64 | 25.1 | 1 | 38
0.32 | 11.8 | 0.68 | 27.3 |  | 

## Slide 9: Rates Velocity
A rate is the quotient of two numbers that are measured using (possibly) different units.
The unit of measure for a rate is the quotient of the units to measure the two numbers.
Example: Driving 120 miles in 2 hours means that you drove 60 miles/hour = 60 miles per hour = 60 mph.
The rate of change of distance over time is called velocity.

## Slide 10: Average Rates of Change
The average rate of change over and interval is the quotient of the change in one variable divided by the change in the other variable.
Example: If the robot is 10 cm from the wall at 0.5 seconds and 16 cm from the wall at 0.7 seconds then the average rate of change over the time between 0.5 and 0.7 seconds is

## Slide 11: Graphing Distance VS Time
We can graph distance VS time.
This generally appears to be a line
It took the robot 0.1 sec or so to start moving.
Chart: Time (sec)
| 0.0 | 0.04 | 0.08 | 0.12 | 0.16 | 0.2 | 0.24 | 0.28 | 0.32 | 0.36 | 0.4 | 0.44 | 0.48 | 0.52 | 0.56 | 0.6 | 0.64 | 0.68 | 0.72 | 0.76 | 0.8 | 0.84 | 0.88 | 0.92 | 0.96 | 1.0
 | 3 | 3 | 3.2 | 4 | 5.8 | 6.7 | 9.3 | 10.3 | 11.8 | 13.7 | 14.9 | 17 | 18.5 | 19.8 | 21.2 | 23.5 | 25.1 | 27.3 | 28.8 | 30.8 | 32.6 | 32.8 | 33.6 | 35.5 | 36.5 | 38

## Slide 12: Graphing Distance VS Time
Beginning at time 0.12 (discarding the first 3 measurements) we get the following graph.
This appears to be generally linear.
Chart: Time (sec)
| 0.12 | 0.16 | 0.2 | 0.24 | 0.28 | 0.32 | 0.36 | 0.4 | 0.44 | 0.48 | 0.52 | 0.56 | 0.6 | 0.64 | 0.68 | 0.72 | 0.76 | 0.8 | 0.84 | 0.88 | 0.92 | 0.96 | 1.0
 | 4 | 5.8 | 6.7 | 9.3 | 10.3 | 11.8 | 13.7 | 14.9 | 17 | 18.5 | 19.8 | 21.2 | 23.5 | 25.1 | 27.3 | 28.8 | 30.8 | 32.6 | 32.8 | 33.6 | 35.5 | 36.5 | 38

## Slide 13: Overall Average Rate of Change
Computing the average of the time from 0.12 sec (4.6 cm) to 0.96 sec (39.1 cm) produces the following rate of change.

## Slide 14: Another Approach
We can also approach this problem from the design end.
The rate of rotations on the motors was set to 700 degrees per second.
The wheels on the robot have a diameter of 5.6 cm (they even have 56 x 28 written on the side of the tire, 56 mm is the diameter 28 mm is the width).
What rate of change would we expect for the robot?

## Slide 15: Expected Velocity
The robot should move 5.6 π for each wheel revolution (circumference of a circle).
If our robot is rotating its wheels at 700 degrees / second, in one second would would expect to travel 700/360 = 1.944 wheel revolutions.
In one second we expect the robot to move 1.944 (5.6 π) = 34.2 cm / sec.
The observed velocity was 38.63 cm / sec. What could be the source of the discrepancy?

## Slide 16: Wheel Model
Suppose we want our robot to turn 90 degrees.
Here is a picture of our robot with some useful measurements.

## Slide 17: Wheel Model
The easiest way to turn to the right would be to drive the left wheel while holding the right will still.
How many degrees should we have the left wheel turn to get close to 90 degrees?
To answer this there are several things to consider.
  What distance will the left wheel need to travel?
  How many degrees of wheel rotation will this take?
  Where on the right tire will the robot pivot?
    Outside edge?
    Inside edge?
    Middle?

## Slide 18: Distance for the Left Wheel

## Slide 19: Distance for the Left Wheel
Assume the right wheel pivots in the middle, the radius of the arc the center of the left wheel travels has a radius of 9.3 + 2.8 = 12.1 cm
The circumference of a circle with this radius is be 2 π 12.1 = 76.03 cm
The left wheel will travel through ¼ of a circle so the distance it travels will be 76.03 / 4 = 19 cm

## Slide 20: Wheel Rotations
We already know the diameter of the tire is 5.6 cm and its circumference is 5.6 π = 17.59 cm.
This means it will take 19 / 17.59 = 1.08 wheel rotation to turn 90 degrees.
Since there are 360 degrees in a complete rotation this means we will need for it to rotate 1.08 (360) = 389 degrees.

## Slide 21: Activity
Write a program to get your robot to turn 90 degrees to the right. Try to do this will as little experimentation as possible using our mathematical model.