## Slide 1: Python Programming
Module 2
Controlling a Lego EV3 Robot

## Slide 2: Download a Program
Before you can run a Python program on your robot you must transfer the program file(s).
Download the programs ev3.py, shortdrive.py, and sensors.py from the Wikispaces page using the Chrome browser.

## Slide 3: Startup EV3
Start up the EV3 brick with the ev3dev SD card inserted.
Connect the EV3 brick to the Chromebook.
  You can use either WiFi or the USB cable.
  See the installation instruction for the details on how to do this.

## Slide 4: Run the Program Wirelessly
Some robot programs work fine while using a USB cable, but if your robot is travelling a long distance you may want to run it wirelessly.
You can connect to the robot using WiFi.
  In this case the IP number used to log into the robot will be different.
You can run programs directly from the EV3 brick using Brickman without any connection.
  See the instructions on how to do this.

## Slide 5: Copy the Program to EV3
Go to Linux on the Chromebook and open a terminal window.
In the terminal window go the the Downloads directory:
  cd ~/Downloads
Copy a file to the EV3 by typing:
  scp ev3.py robot@192.168.0.1:.
  You will need to change the number here to match the number on your EV3 brick.
Enter the password: maker
Repeat this twice more copying shortdrive.py and sensors.py to the EV3.

## Slide 6: Run the Program
Next in the terminal window type:
  ssh robot@192.168.0.1
  Again you may need to change the numbers.
Reenter the password: maker
Notice the prompt changes to “robot@ev3dev”; this means command you type will go to the EV3.
You can now run the program by typing:
  python3 shortdrive.py
The robot should drive a short distance, turning to the right.

## Slide 7: Plugging in Motors
In order to use motors, they must be plugged into the output ports on the EV3 brick.
The output ports are labeled A, B, C, and D on the brick.
In these examples we will assume that two large motors are plugged into ports B and C.
  These will be the “Left motor” and the “Right motor” respectively.

## Slide 8: Loading Libraries
Let’s look at what is in the program file.
Python is a general purpose language and was not designed with robots in mind.
We need to load in modules that contain the bindings connect function calls to the motors.
  from ev3 import *
This loads in the ev3.py file.
  from time import sleep

## Slide 9: Naming the Motors
Next we create a variable name for each motor.
We will send messages to the motor using these names.
  #connect the motors
  motorLeft = LargeMotor('outB')
  motorRight = LargeMotor('outC')
Since we have two Large Motors we must specify the port name of each.

## Slide 10: Setting the Run Time
The motors operate independently so we must set the run time for each of them.
We do this by setting a parameter associate with each motor.
  #set the run time to 5 sec
  motorLeft.time_sp = 5000
  motorRight.time_sp = 5000
Note the run time is in milliseconds

## Slide 11: Set the Power Level
Next we set the power level (wattage) for each motor.
Generally this corresponds to speed, but there is a different mode where speed is directly measured and controlled.
The values for this parameter range from -100 (100% backward) to 100 (100% forward).

## Slide 12: Set the Power Level
The power level can be different for each motor.
This will cause the robot to turn.
  #set the power level for each motor
  #Right has more power
  #Robot turns left
  motorLeft.duty_cycle_sp = 75
  motorRight.duty_cycle_sp = 100

## Slide 13: Run the Motors
Now that we know the duration and power level for each motor, we are ready to run them.
There are many options here, which we will discuss in a moment.
  #run the motors
  motorLeft.run_timed()
  motorRight.run_timed()

## Slide 14: Wait for the Robot to Stop
The motor will stop when 5 seconds are up or when the program ends – whichever comes first.
We need to wait for the 5 seconds before quitting.
  #wait for the robot to stop
  sleep(5)

## Slide 15: Timing
Notice that we started the left motor before the right motor.
  The real world time between these two start times is too small to notice.
Also notice that we can have multiple motors running at the same time.
  This is one advantage of Python over the Lego Software – it is easier to have the robot do two things at once.

## Slide 16: Medium Motors
In addition to Large Motors we also have Medium Motors.
All of the motors are controlled in the same way except that when we name the motor we would use the following:
  m = MediumMotor(‘outA’)
If your robot only has one Medium Motor you could also use:
  m = MediumMotor()

## Slide 17: Why Two Different Motors?
Large Motor:
  Faster
  More overall power
Medium Motor
  Slower
  Higher torque
  More precise control

## Slide 18: Motor Commands
There are several ways to control how long a motor runs.
  run_timed – run for time_sp milliseconds.
  run_forever – run until told to stop.
  run_stop – stop the motor.
  run_to_rel_pos – run the motor position_sp degrees.
There are a few others, but this is a start.

## Slide 19: Motor Parameters
There are also several parameter you can set to determine how the motor behaves.
  time_sp – how long to run (milliseconds).
  duty_cycle_sp – how much power to use [-100, 100].
  polarity – which direction is positive (‘normal’, ‘inversed’).
  position_sp – how many degrees to rotate.

## Slide 20: Motor Parameters
  ramp_down_sp – as the motor approaches its goal, how long to slow down (milliseconds).
  ramp_up_sp – as the motor starts, how long to speed up (milliseconds).
  speed_regulation_enabled – vary the power to hold a constant speed (‘on’, ‘off’).
  speed_sp – how fast to go when using speed regulation (degrees per second).

## Slide 21: Motor Parameters
  stop_command– how to stop:
    ‘coast’ – remove power and freely coast
    ‘brake’ – place a load on the motor to absorb energy and stop more quickly.
    ‘hold’ – after stopping actively try to hold position by using power to “fight” any attempt to move it.

## Slide 22: Activities
Experiment and see how close you can to having your robot do the following:
Drive in a straight line forward 1 meter.
Drive backward 1 meter.
Spin in place (drive one wheel forward and the other backward).