## Slide 1: Python Programming
Module 4
Sensors and Loops

## Slide 2: Sensors
In addition to the temperature sensor we have the following sensors:
  Touch Sensors (2) – a button that can tell when it is pressed.
  Color/Light Sensor – an optical sensor that senses ambient light or reflected color.
  Ultrasonic Sensor – uses echo location to determine its distance from an object.
  Gyro Sensor – uses accelerometers to measure its rotation about a particular axis.

## Slide 3: Attaching Sensors
You must plug the sensors into the input ports on the EV3 brick.
These are the ports labeled 1, 2, 3 and 4.
When you name a sensor in Python you can auto detect the sensor.
  touch=TouchSensor()

## Slide 4: Attaching Sensors
You may need to specify the port if you are using the Temperature Sensor or if you are using more than one of the same type of sensor.
  touchL = TouchSensor(‘in1’)
  touchR = TouchSensor(‘in4’)
The input ports are named ‘in1’, ‘in2’, ‘in3’ and ‘in4’.

## Slide 5: Reading Sensors
Once you have the sensor attached and named you can read what it is currently sensing using its value function.
  u = UltrasonicSensor()
  u.value()
This will report a distance, but what are the units?
The sensors all have different modes that determine the units used.

## Slide 6: Setting Sensors Modes
To determine the units you can do the following:
  u = UltrasonicSensor()
  u.mode = ‘US-DIST-CM’
  u.value()
Now the results will be in 10th of a centimeter (millimeter).
If the value is 324 this corresponds to 32.4 cm.

## Slide 7: Sensor Modes
Touch Sensor – no modes. The value is 0 when the button is not pushed and 1 when pushed.
Ultrasonic Sensor – the value is a distance.
  ‘US-DIST-CM’ – distance measured in 10th of a centimeter
  ‘US-DIST-IN’ – distance measured in 10th of an inch.

## Slide 8: Sensor Modes
Gyro Sensor – the value is a rotation.
  ‘GYRO-ANG’ – measures the relative number of degrees rotated since the sensor was initialized.
  ‘GYRO-RATE’ – measures the rate at which the sensor is rotating in degrees/second.

## Slide 9: Sensor Modes
Color Sensor – measures light intensity and color.
  ‘COL-REFLECT’ – measures reflected light intensity 0-100.
  ‘COL-AMBIENT’ – measures ambient light intensity 0-100.
  ‘COL-COLOR’ – measures color
    0 none 3 green 6 white
    1 black 4 yellow 7 brown
    2 blue 5 red

## Slide 10: Sensors and Motors Interacting
We now know how to run motor and how to read a value from a sensor.
We need to figure out how to write programs where the value read by the sensor will determine what action the motors take.
We need to be able to control what instructions are done and when they are done.

## Slide 11: Flow Control
Python Provides three basic structures to control the order in which program statements are executed.
  if – else structure
  while loop
  for loop
We will look at each of these but let’s start with the while loop.

## Slide 12: While Loops
A while loop repeats some block of code (called its body) over and over again until a particular condition becomes false.
For example: Drive the robot forward while the distance from the wall is greater than 5 cm.
  i.e. drive until you are 5 cm from the wall.
Notice we do not know how long this will take, so this is called an indefinite loop.

## Slide 13: Indefinite Loops
while <condition>: <body>
<condition> is a Boolean Statement that is either true or false. The body is a sequence of one or more statements.
The <body> of the loop executes repeatedly as long as the condition remains true. When the condition is false, the loop terminates.

## Slide 14: Indefinite Loops
The condition is tested at the top of the loop. This is known as a pre-test loop. If the condition is initially false, the loop body will not execute at all.

## Slide 15: Boolean Statements
A Boolean statement is one that is either true or false.
It is usually constructed by comparing two mathematical expressions.
A simple comparison might look like the following:
  <expr> <relop> <expr>
Here <relop> is short for relational operator.

## Slide 16
Python | Mathematics | Meaning
< | < | Less than
<= | ≤ | Less than or equal to
== | = | Equal to
>= | ≥ | Greater than or equal to
> | > | Greater than
!= | ≠ | Not equal to
Relational Operators

## Slide 17: Check for Equality
Notice the use of == for equality. Since Python uses = to indicate assignment, a different symbol is required for the concept of equality.
A common mistake is using = in conditions when you really want == !

## Slide 18: Forming Simple Conditions
Boolean conditions are of type bool and the Boolean values of true and false are represented by the literals True and False.
>>> 3 < 4
True
>>> 3 * 4 < 3 + 4
False
The expressions on either side of the operator can contain variables and/or the results of functions.
  u.value() > 0.5

## Slide 19: Driving and Stopping
Using a sensor and two motors and a while loop we can drive our robot until we approach an object.
What we will do is set both motor to run until they are stopped (run_forever).
We will then enter a loop that will end when the robot is 5 cm from some obstruction.
We don’t need to actually do any work in this loop so the body will be the placeholder command pass.
After we get out of the loop we stop the motors.

## Slide 20: Driving and Stopping
  from ev3 import *
  motorL = LargeMotor('outB')
  motorR = LargeMotor('outC')
  ultra = UltrasonicSensor()
  ultra.mode = 'US-DIST-CM'
  motorL.run_forever(duty_cycle_sp = 50)
  motorR.run_forever(duty_cycle_sp = 50)
  while(ultra.value() > 50):
  pass
  motorL.stop()
  motorR.stop()

## Slide 21: Activities
Write a program that will pause the robot while an obstruction is within 5 cm. When the obstruction is removed, the robot will begin driving and stop when it gets within 5 cm of another obstruction.
Write a program that makes the robot run while the button on the touch sensor is pushed.
Write a program that will cause the robot to begin moving when the color sensor “sees” green and stops the robot when it “sees” the red.