## Slide 1: Python Programming
Module 6
Making Decisions

## Slide 2: Simple Decisions
We have seen how we can use loops and a sensor to make a robot stop or start doing something.
In many cases we need to make a decision.
  Do this if we see “red”.
  Do that if we see “blue”.
Python provides an if-else structure that we can use to do this.

## Slide 3: Example: Temperature Warnings
Let’s return to our Temperature Sensor program from Module 5.
from time import sleep
  from ev3 import *
  from numpy import mean, std
  t_sensor = TemperatureSensor('in1')
  t_sensor.mode = 'TEMP-C'
  temps = []
  for i in range(10):
  temps.append(t_sensor.value())
  sleep(1)

## Slide 4: Reading and Storing Temperatures
print('Temperatures:')
  for x in temps:
  print(x)
  print('Mean: ', mean(temps))
  print('Standard Dev: ', std(temps))
Let’s say we want to modify the program to print a warning when the temperature is extreme.
Any temperature over 30 degrees and lower than 15 degrees Celsius will cause hot or cold warnings respectively.

## Slide 5: Example: Temperature Warnings
Read the temperature in degrees Celsius (call it celsius)
If celsius > 30 print a heat warning
If celsius < 15 print a cold warning
This new algorithm has two decisions. The indentation indicates that a step should be performed only if the condition listed in the previous line is true.

## Slide 6: Example: Temperature Warnings

## Slide 7: Example: Temperature Warnings
from time import sleep
from ev3 import *
from numpy import mean, std
t_sensor = TemperatureSensor('in1')
t_sensor.mode = 'TEMP-C'
temps = []
for i in range(10):
celsius = t_sensor.value()
if celsius > 30:
print("I'm feeling the heat!")
if celsius < 15:
print("Why the cold shoulder?")
temps.append(celsius)
sleep(1)

## Slide 8: Example: Temperature Warnings
print('Temperatures:')
for x in temps:
print(x)
print('Mean: ', mean(temps))
print('Standard Dev: ', std(temps))
This program is very similar to the previous one except that it prints a warning if the temperatures are high or low.
Instead of printing we could do something else: beep, flash a light, move, etc.

## Slide 9: Python If Statement
The Python if statement is used to implement the decision.
if <condition>: <body>
The body is a sequence of one or more statements indented under the if heading.

## Slide 10: Python If Statement
The semantics of the if should be clear.
  First, the condition in the heading is evaluated.
  If the condition is true, the sequence of statements in the body is executed, and then control passes to the next statement in the program.
  If the condition is false, the statements in the body are skipped, and control passes to the next statement in the program.

## Slide 11: Nesting
Notice that the if statements are located inside a for loop.
Their conditions will be tested once each time the loop executes.
This is an example of nesting control structures.
All control structures can be nested as necessary to do complicated jobs.

## Slide 12: Activity
Write a program that will control a robot that uses the Ultrasonic Sensor. The robot wants to drive forward but not through an obstruction.
  If the robot is within 10 cm of an obstruction, have the robot turn 90 degrees to the right.
  Next, have the robot drive forward until it is within 10 cm of a new obstruction.

## Slide 13: State Variables
It is often helpful to have variables that keep track of one of the modes of our robot.
An example would be the units to use when reporting a temperature.
  temp = TemperatureSensor(‘in2’)
  temp.mode = ‘TEMP-F’
Here temp.mode is a state variable that keeps track of the appropriate units to use for this temperature sensor.

## Slide 14: State Variables
We can use if statements with state variables to determine the appropriate behavior of our robot.
if temp.mode == ‘TEMP-F’:
#return temperature in degrees Fahrenheit
if temp.mode == ‘TEMP-C’:
#return temperature in degrees Celsius
if temp.mode == ‘TEMP-K’:
#return temperature in degrees Kelvin
You may also want a state variable to “remember” what your robot should be doing right now: searching for something, returning home, waiting for something to happen, etc.

## Slide 15: Two-Way Decisions
Often we have two mutually exclusive options.
As an example a Touch Sensor is either pressed or it is not.
We could have the robot do one thing when the sensor is pressed and something else if it is not pressed.
We could use two if statements but that would be sloppy.

## Slide 16: Two-Way Decisions

## Slide 17: Two-Way Decisions
In Python, a two-way decision can be implemented by attaching an else clause onto an if clause.
This is called an if-else statement: if <condition>: <statements> else: <statements>

## Slide 18: Two-Way Decisions
When Python encounters this structure, it first evaluates the condition. If the condition is true, the statements under the if are executed.
If the condition is false, the statements under the else are executed.
The program will pick up with the statements that follow the if-else after either the statements in the if or the else are executed.

## Slide 19: Right-on-Red Example
The following program uses the Touch Sensor and the Color Sensor.
The robot waits for the button on the Touch Sensor to be pressed.
Next the robot checks the color detected by the color sensor.
  If the color sensor sees “red” then the robot spins to the right.
  Otherwise the robot spins to the left.
  You can use red Legos to test this.

## Slide 20: Right-on-Red Example
from ev3 import *
from time import sleep
motorL = LargeMotor('outB')
motorR = LargeMotor('outC')
color = ColorSensor()
touch = TouchSensor()
while(touch.value() == 0):
pass

## Slide 21: Right-on-Red Example
color.mode = 'COL-COLOR'
if color.value() == 5:
motorL.duty_cycle_sp = 50
motorL.time_sp = 5000
motorL.run_timed()
else:
motorR.duty_cycle_sp = 50
motorR.time_sp = 5000
motorR.run_timed()
sleep(5)

## Slide 22: Activity